Observations of the process of developing MIMO. The goal, at this point, is to minimize the amount of template haskell and thereby clarify the structure of the system. Until recently the structure had been several stages of template haskell. I developed a few techniques to convert this to a flatter structure:

1. Replace use of imports of code generated by TH with an extra parameter holding record containing those values. Then once the imports are all converted to uses of the record fields, the function can be moved to the library. This leaves behind the actual invocations of the moved functions, which is short and can be collected into fewer modules.
2. Turn uses of types stored in the info record into type parameters.

Things to keep in mind:

You can’t mix hsx2hs and template haskell splicing. So its good to confine the latter as much as possible.